## Slide 1: Costing Renewable Energy and Storage in Australia: GenCost and the Renewable Energy Storage Roadmap
Dr Jenny Hayward | 16 October 2024
Notes: The methodology behind our cost projections, which I’ll be talking about today, has been applied to the Australian context. However, the same methodology can be applied to project costs for any country or region

## Slide 2: GenCost

## Slide 3: GenCost context – purpose and history
Delivered since 2018 in partnership with the Australian Energy Market Operator (AEMO).
The purpose is to provide an annual update of current and projected electricity generation, storage and hydrogen technology costs.

## Slide 4: GenCost project outputs
GenCost outputs
Capital cost projections
Current cost update
LCOE
Standard formula
Variable renewables methods
GALLM projection model
Data for the modelling community and AEMO (e.g. ISP, ESOO)
Methods
Users
Non-modelling community
Outputs
Notes: Eli talked about the ISP this morning, and our cost projections are one of the key inputs as costs are one of the key determinants of which technologies are installed.
James is going to be talking about the levelised cost of electricity LCOE

## Slide 5
Methods for projecting technology costs
Expert surveys
Historical rate extrapolation
Bottom-up engineering
Consensus building
Learning by doing / simulation
Basis of views not transparent. Likely to include some bias in response selection
Benchmarked
Does not provide rationale for divergence from historical rates
Simple, easy to follow
Change is a function of time only – bottlenecks or stalled development not included
Strong basis in physical limits and science
Provides deep guidance on cost and science challenges
Costly. Typically delivered one technology at a time
Transparent and strong basis for projections. But lacks science insights.
Better able to project fast cost reductions of emerging technologies
Computationally demanding

## Slide 6
CSIRO approaches
Expert surveys
Historical rate extrapolation
Bottom-up engineering
Consensus building
Learning by doing / simulation
Basis of views not transparent. Likely to include some bias in response selection
Benchmarked
Does not provide rationale for divergence from historical rates
Simple, easy to follow
Change is a function of time only – bottlenecks or stalled development not included
Strong basis in physical limits and science
Provides deep guidance on cost and science challenges
Costly. Typically delivered one technology at a time
Transparent and strong basis for projections. But lacks science insights.
Better able to project fast cost reductions of emerging technologies
Computationally demanding


CSIRO Global and Local Learning Models
Established technologies e.g. gas turbines


## Slide 7: Projected global technology mix
The global technology mix and capital cost reductions are simultaneously projected

## Slide 8: Battery storage system cost projections
On a total cost basis.
2 hours of storage.
We also modelled 1, 4, 8, 12 and 24 hours.

## Slide 9: Pumped hydro storage cost projections
On a total cost basis.
12 hours of storage.
We also modelled 6, 8, 12, 24 and 48 hours.

## Slide 10: Renewable Energy Storage Roadmap
Notes: This is an example of where we use our cost projections from GenCost. We use our cost projections in other studies we undertake in CSIRO

## Slide 11: A toolkit for decision making
Estimate electricity, hydrogen and thermal storage demand across scenarios and jurisdictions
Understand specific energy storage requirements across 7 sectors.
Examine the role of storage, deployment considerations and technology options
Estimate the levelised cost of storage (LCOS) across different storage options
Understand action steps to efficient scale-up and deployment of energy storage in Australia

## Slide 12
Levelised cost of storage

## Slide 13: Understanding the comparative costs between storage technologies options is complex and critical for investment decisions
ENERGY INPUT COSTS
COSTS RELATED TO CHARGING OF SYSTEM
COSTS RELATED TO STORAGE OF ENERGY
COSTS RELATED DISCHARGING OF ENERGY
CAPITAL AND BALANCE OF PLANT
LCOS
Levelised cost of storage (LCOS)
  LCOS is defined as the sum of discounted costs per unit of delivered energy over an investment’s lifetime, which is equivalent to the average price at which electricity can be sold for the storage investment’s net present value to be zero.
  The approach disaggregates the energy generation and transmission system costs from storage costs to better understand the drivers of storage cost components.
Notes: Key point to note with calculating the levelised cost of storage is that it is heavily dependent on how the storage is used. Therefore, you need to compare different technologies under the same storage usage case, which I’ll talk about next.

## Slide 14: Remote grids: Mining and communities Significant emissions reductions are possible in the near term, but long-duration storage will be key to higher levels of decarbonisation
VRE and short duration storage can provide significant emissions reductions in the near term
Chart: 
| Sunny community | Windy community | Remote mining
VRE+Short-duration storage | 0.48 | 0.8 | 0.42
Diesel | 0.52 | 0.2 | 0.58
Remote mining case
Remote community A
Remote community B
However, long-duration storage technologies are required to displace diesel and achieve greater emissions reductions
​Remote community B (strong solar resources):
163 hours of long duration storage (2.5 MW), used 14 times per year, on average.
Remote mining
36 hours of long duration storage (93 MW) used once per week.
Remote community A (strong wind resources):
48 hours of long duration storage (5 MW) used 20 times per year on average.
Notes: James will be discussing the NEM and WA grid case studies during his presentation

## Slide 15: Remote mining case study – Northwest WA
Largely flat load with an average of 45MW and a peak of 48MW.
Day-to-day variability of 19.3%
Currently using 200MW PV with remainder from diesel.
PV supplies the majority of the daily load – 42% of site load in total.
Technologies:
  PHES – depends on geography and water
  CST - suitable solar resource
  A-CAES and underground H2 storage – depends on geology
  Compressed H2 tanks and eTESe – flexible technologies

## Slide 16: Remote mining case study - results
Short duration battery storage – 30 minutes with 102 full discharges/year
Long duration CST – 93MW/3.3GWh or 36 hours with 52 full discharges/year

## Slide 17: Thank you
CSIRO Energy
  Jenny Hayward
    jenny.hayward@csiro.au
Notes: Thank you all for joining. We are more than happy to discuss the Roadmap findings so please do reach out.

## Slide 18
Concept of Technology Learning
- Example PV modules
Source: Fraunhofer ISE

## Slide 19: LCOS components
Each LCOS is divided into four subcomponents, converted into a common unit ($/MWh) in the calculation
  Energy input costs: this is the required output + any losses
  Power capital cost: cost of charging and discharging the system
  Energy capital cost: the storage component
  OPEX: calculated as a percentage of total installed CAPEX
ENERGY INPUT COSTS
COSTS RELATED TO CHARGING OF SYSTEM
COSTS RELATED TO STORAGE OF ENERGY
COSTS RELATED DISCHARGING OF ENERGY
CAPITAL AND BALANCE OF PLANT
LCOS
Notes: Pumped hydro example:
2. Power capital cost: For example, for a pumped hydro system this includes pumps to raise the water to the dam, the tunnel/pipes for water transfer and a turbine for generation.
3. Energy capital cost: For a PHES this includes the water storage dams.

## Slide 20: LCOS economic and technical assumptions