## Slide 1: System Security – Distributed PV Backstop
17 October 2024
Alex Ward
Future Networks Program Manager
SA Power Networks

## Slide 2: South Australia’s renewable milestones
-26MW Minimum Demand and 100% Rooftop Solar
2.5GW of Rooftop PV
More than 1 in 3 customers have solar
70% of Annual Generation met by Renewables
1.5GW Average Demand

## Slide 3: Our Flexible Exports offer
Customers with smart inverters can receive a flexible export limit
Choice between
  Fixed export 1.5kW/phase
  Flexible Exports 1.5-10kW/phase
Export limits at 10kW for 95% of customers 95% of the time

## Slide 4: Our journey with flexible solar
2019
2021
2017
2022
1 July
2023
Reset proposal
$32m Capex
$3.8m Opex
First test with
Tesla VPP
1000 batteries
‘Grid of the Future’
Embedded IT team, new agile delivery
Customer Offer, Customer Journey, System design and Implementation plan
2018
Concept and early engagement
Flexible Exports for Solar PV trial
>400 customers
‘Dynamic Exports’ SA Gov. Regulations announced
National technical standard published
Scale up team established
SA Gov. Regulations in effect
Flexible Exports rollout commences
SAPN enables technical and regulatory implementation
2020

## Slide 5: Helping facilitate a national rollout
National cyber security framework
National equipment standards, testing and certification
A consistent, national approach to CER integration will be least cost for customers and industry

## Slide 6: Why use Dynamic Operating Envelops for DPV Curtailment?
Several advantages over other mechanisms:
Fail safe behaviour when comms is lost (protects network and incentivises connectivity)
Incentive to commission site correctly (access to 10kW export)
Real-time feedback of system response (SAPN, installer and customer)
Enables ancillary response from storage

## Slide 7
Transition to flexible DER
Flexible Exports will be rolled out across SA from July 2023 – December 2024
We’re on the path for all solar to be fully flexible by 2030

## Slide 8: CER compliance improvement
Install
Apply
>90%
Of a solar retailers sites must be compliant
Compliance
40%
95%
Compliance
Once installers are engaged, they generally want to do the right thing
Compliance incentives and penalties must be aligned to the right parties
Has led to…
Commission
Install
Closeout
Transformed our process
Introduced automated compliance program

## Slide 9
Time
Export Limit (kW)
10:00
2
4
6
8
10
11:00
12:00
1:00
2:00
3:00
4:00
5:00
6:00
7:00
4x 15-minute events: forecasted network constraints
Decaying confidence schedule of 1-hour controls
Take last constraint
80% for 1 hour
60% for 1 hour
40% for 1 hour
1.5kW failsafe
DefaultDERControl
DERControl
IEEE 2030.5 Resources
DER Control events have a finite start time and duration
DefaultDERControls have no start or end time and are persisted through restarts.
Applied when no DER Controls are present e.g. during communications outage.

## Slide 10: Structuring the program – A multi- disciplinary effort
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr
Sales | 0.3 | 0.3 | 0.3
Engineering, technology and systems
Stakeholder and customer engagement
Internal business capability

## Slide 11: CSIP-AUS Journey
IEEE 2030.5:2018 Communications protocol for smart energy devices.
Contains 16 function sets
Common Smart Inverter Profile – (CSIP) Implementation guide for network to DER smart inverter integration with a subset of optional function sets
Common Smart Inverter Profile – Australia (CSIP-AUS) Additional extensions to support site level DOE use cases, written as deltas to CSIP.

## Slide 12: 2022: DPV Control in Action – State Response
SCADA generators
Emergency Voltage Raise
Smarter Homes
(& Flexible Exports)
Control mechanisms:
91.5% peak VRE while islanded
SA was islanded from the NEM November 2022 for 7 days
DPV curtailment required on 6 days to keep the system stable

## Slide 13: 2022: DPV Control in Action – Customer Experience
Export limit
Friday 11 Nov:
Export limit reduced due to local network congestion
Saturday 12 Nov:
Power outage due to storm event
Comms interrupted
Sunday 13 Nov:
Power restored
Comms online
Monday 14 Nov:
Export constrained from 10kW to 0kW to maintain system security on AEMO direction
Solar self-consumption continues
Grid import
Grid export
Export limits at 10kV >98% of the time

## Slide 14: 2024: DPV Control in Action
SCADA generators
Emergency Voltage Raise
Smarter Homes
(only Flexible Exports)
Control mechanisms:
5MW curtailed via Flexible Exports Emergency Controls
Control execution speed: 15min
High response rate: 85% of devices curtailed
Several transmission towers failed in Victoria in February 2024
DPV curtailment required for 2 hours to keep the system stable