## Slide 2: Historical electricity grid
DNO
Inflexible demand side
Flexibility
“Passive” network
No generation
Transmission system
Distribution network
Radial networks
Extremely high value of customer reliability -> No congestions
Meshed networks
Price arbitrage opportunities across network nodes
Economically optimal to have congestions
All generation
Fully dispatchable and controllable
Control problem solved at the planning stage: worst-case design
Integrated planning of generation and transmission

## Slide 3: A Copernican revolution for the grid
Image taken from the internet

## Slide 4: A Copernican revolution for the grid
DNO
No generation
Transmission system
Distribution network
Inflexible demand side
Invisible embedded generation
=
Negative demand
“Passive” network

## Slide 5: A Copernican revolution for the grid
DNO
No generation
Transmission system
Inflexible demand side
Invisible embedded generation
=
Negative demand
“Active” network
Distribution network
Congestions emerge!

## Slide 6: A Copernican revolution for the grid
DNO
No generation
Transmission system
Invisible embedded generation
=
Negative demand
“Active” network
Distribution network
Inflexible demand side
Electrification for energy efficiency and decarbonisation

## Slide 7: A Copernican revolution for the grid
DNO
No generation
Transmission system
Invisible embedded generation
=
Negative demand
“Active” network
Distribution network
We should develop integrated planning of distribution systems and DER
Flexible demand side

## Slide 8: Electrification and network benefits of DER management schemes
G. Strbac et al., “Benefits of Advanced Smart Metering for Demand Response based Control of Distribution Networks”, Imperial College London, 2010

## Slide 9: Electrification and network benefits of DER management schemes
G. Strbac et al., “Benefits of Advanced Smart Metering for Demand Response based Control of Distribution Networks”, Imperial College London, 2010
Notes: In the Imperial study, PV was not in the analysis. Now, with PV and batteries, we have huge further opportunities for both decarbonisation and further reduction of energy needed from the transmission grid and of the peak

## Slide 10: A Copernican revolution for the grid
DNO
No generation
Transmission system
Invisible embedded generation
=
Negative demand
“Active” network
Variable and partly unpredictable
Distribution network
Flexible demand side

## Slide 11: A Copernican revolution for the grid
DNO
No generation
Transmission system
Flexible demand side
Potentially visible, controllable and dispatchable
DER, VPP, Energy communities, Microgrids
Variable and partly unpredictable
Flexibility
“Active” network
Distribution network

## Slide 12: A Copernican revolution for the grid
DNO
No generation
Transmission system
Distribution system
Flexible demand side
Potentially visible, controllable and dispatchable
“Active” system
DER, VPP, Energy communities, Microgrids
Variable and partly unpredictable
Flexibility
DSO

## Slide 13: Role of the demand side in the future
Installed generation capacity, “Step change” scenario
Source: AEMO, ISP 2024

## Slide 14: A Copernican revolution for the grid
DNO
No generation
Transmission system
Distribution system
Flexible demand side
Potentially visible, controllable and dispatchable
Variable and partly unpredictable
Flexibility
DSO
“Active” system
DER, VPP, Energy communities, Microgrids

## Slide 15: A Copernican revolution for the grid
DNO
No generation
Transmission system
Distribution system
Flexible demand side
Potentially visible, controllable and dispatchable
Variable and partly unpredictable
Flexibility
DSO
“Active” system
DER, VPP, Energy communities, Microgrids
Notes: To decarbonise heating, hot water and transport, you’ll have massive storage available
Perfect combination with distributed PV, in case with (community) batteries
What is the optimal storage portfolio
The integrated system problem can be seen as an optimal storage portfolio design problem
Talking about pumped hydro completely neglect the problem of networks
  Continues being supply-centric rather than consumer-centric

## Slide 16: How much and what storage do we need?
F. Cebulla, et al., “How much electrical energy storage do we need?”, Journal of Cleaner Production, Volume 181, 20 April 2018, 449-459
GW
GWh
Renewables penetration
Correlation with generation type matters!

## Slide 17: A Copernican revolution for the grid
DNO
No generation
Transmission system
Distribution system
Flexible demand side
Potentially visible, controllable and dispatchable
Variable and partly unpredictable
Flexibility
DSO
“Active” system
We should develop integrated planning of transmission and distribution systems and large-scale resources and DER
DER, VPP, Energy communities, Microgrids
Notes: To decarbonise heating, hot water and transport, you’ll have massive storage available
Perfect combination with distributed PV, in case with (community) batteries
What is the optimal storage portfolio
The integrated system problem can be seen as an optimal storage portfolio design problem
Talking about pumped hydro completely neglect the problem of networks
  Continues being supply-centric rather than consumer-centric

## Slide 18: Integrated planning of transmission and distribution systems with DER
1
2
3
“Passive” distribution network
C. Alcarruz et al., “Integrated transmission and distribution expansion planning: A critical overview”, 2024, under preparation

## Slide 19: Integrated planning of transmission and distribution systems with DER
1
2
3
“Passive” distribution network
C. Alcarruz et al., “Integrated transmission and distribution expansion planning: A critical overview”, 2024, under preparation

## Slide 20: From passive to active distribution system
Source: M. Liu et al., “Grid and market services from the edge”, IEEE Power and Energy Magazine, July/August 2021

## Slide 21: Integrated planning of transmission and distribution systems with DER
1
2
3
“Passive” distribution network
C. Alcarruz et al., “Integrated transmission and distribution expansion planning: A critical overview”, 2024, under preparation

## Slide 22: Integrated planning of transmission and distribution systems with DER
1
2
3
ADS
ADS: Active Distribution System
ADS
ADS
C. Alcarruz et al., “Integrated transmission and distribution expansion planning: A critical overview”, 2024, under preparation
Notes: Cost function methodology
Passive planning
Active distribution system management
Different types of storage (incl. community) and CER orchestration
  Non-network solutions
  EV and EHP orchestration
Cost of orchestration and ADSM
Importance of community “generation” and FOM storage – see recent ENA report

## Slide 23: But what future do we plan for?
Source: AEMO, ISP 2020
Notes: Central scenario: reduction of consumption forecast growth in EE savings, lower EV impact, and improved representation of structural shifts in energy consumption
Step change scenario: higher economic activity, population growth, and greater electrification of the transport sector are forecast to be balanced by consumer-led investment in PV, EE measures, and a greater orientation towards economic activity from less energy-intensive manufacturing activities

## Slide 24: Lots of futures…
Source: AEMO, ISP 2024
Notes: DER also allows

## Slide 25: Shall we plan for the expected future?

## Slide 26: We plan for the expected but fear the extreme…
https://www.aemc.gov.au/sites/default/files/2022-08/Pierlugi%20Mancarella%20-%20Briefing%20note%20-%20form%20of%20the%20reliability%20standard.pdf
Notes: Extreme is technical and economic

## Slide 27
See : P. Mancarella, et al., “Study of advanced modelling for network planning under uncertainty - Part 1”, Report for National Grid ESO, 2020: https://www.nationalgrideso.com/document/185821/download
Risk-aware decision under uncertain scenarios
Least-Worst Weighted Regret
(LWWR) analysis

## Slide 28: But the modern integrated system investment problem is much more complicated….
Source: https://clockwise.software/blog/solve-the-chicken-and-egg-problem/

## Slide 29: Need for proactive, anticipatory network investment
Source: AEMO ISP 2020 and Environment Victoria
Notes: RES takes one year, transmission five years
We then need anticipatory investment
But in the classical chicken and egg problem we need risk analysis, particularly to avoid large risk in stranded asset, we
Distt networks and DER has the same problems because of the regulatory cycles
DER can be built very fast
Distribution networks cannot
  Subject to regulatory processes and cycles
Several issues not captured at the transmission level
Distribution network planning is very complex when considering active distribution system management and non-network solutions, incl. DER and CER

## Slide 30
Non-network solutions cannot be
appropriately valued deterministically
R. Moreno, et al., “Planning Low-Carbon Electricity Systems under Uncertainty Considering Operational Flexibility and Smart Grid Technologies”, Philosophical Trans. Royal Society A, June 2017
Notes: Stochastic planning gives you the ODP across all potential combination of scenarios
Much more robust investment
More certain here and now investment
Anticipatory investment
DER to manage uncertainty

## Slide 31: ISP under uncertainty
SQ-CNQ Option 1
SQ-CNQ Option 2
SQ-CNQ Option 3
CNQ-SQ Option 4
NNSW–SQ Option 1
NNSW–SQ Option 2
NNSW–SQ Option 3
NNSW–SQ Option 4
CNSW-NNSW Option 1
CNSW-NNSW Option 2
CNSW-NNSW Option 3
CNSW-NNSW Option 4
CNSW-NNSW Option 5
CNSW-NNSW Option 6
CNSW-NNSW Option 6A
CNSW-NNSW Option 6B
CNSW-NNSW Option 7
CNSW-NNSW Option 8
CNSW-NNSW Option 9
CNSW-NNSW Option 10
VIC-SNSW Option 1 - VNI West
VIC-SNSW Option 2 - VNI West
VIC-SNSW Option 6A
VIC-SNSW Option 6
VIC-SNSW Option 7
TAS-VIC Option 1
TAS-VIC Option 2
SNSW-CNSW Option 1
SNSW-CNSW Option 2
SNSW-CNSW Option 3
CNQ-GG Option 1
CNSW-SNW Option 1
CNSW-SNW Option 2
CNSW-SNW Option 3
H-Newcastle
H-Dapto
Project EnergyConnect
30
13
31
16
17
7
8
18
19
20
21
22
24
25
10
26
27
11
28
2
4
12
29
14
32
1
3
5
2022 | 2027 | 2032 | 2037
Slow
Progressive
Step
H2
15
6
9
23
0.50
0.29
0.17
0.33
0.50
0.33
0.50
0.17
0.83
0.17
1.00
0.17
0.83
0.17
1.00
1.00
1.00
0.83
0.17
0.04
0.21
0.29
0.50
0.21
0.29
0.50
0.33
0.50
0.17
0.83
0.17
Notes: 4-stage tree – 32 nodes
18 equivalent scenarios

## Slide 32: Comparison between stochastic and LWWR optimal development paths
A stochastic plan enables identification of investment portfolios with better techno-economic performance against different future scenarios
32N1W representation
expected
Notes: Stochastic planning reduces the expected cost

## Slide 33: Comparison between stochastic and LWWR optimal development paths
32N1W representation
worst-case
expected
Also limiting risk!
A stochastic plan enables identification of investment portfolios with better techno-economic performance against different future scenarios
Notes: Stochastic planning also reduces the worst case cost (and regrets!)

## Slide 34: Integrated planning under uncertainty of transmission and DER
1
2
3
ADS
ADS: Active Distribution System
ADS
ADS
P. Apablaza et al., “Assessing the Impact of DER in the Expansion of Low-Carbon Power Systems Under Deep Uncertainty”, Electric Power System Research, 2024
DER with orchestration and transmission-level investment exhibit complementarity and synergy
Benefits from DER orchestration better captured when considered planning uncertainty and network investment risk
DER orchestration may systematically reduce transmission-level:
  investment requirements
  investment uncertainty → risk-hedge value

## Slide 35: Capturing the value of DER resilience
Moreno, R., et al. (2022). Microgrids Against Wildfires: Distributed Energy Resources Enhance System Resilience. IEEE Power and Energy Magazine, 20(1), 78-89.

## Slide 36: Whole-system planning beyond electricity! Integrated electricity-gas-hydrogen modelling
I. Saedi, et al., “Integrated Electricity and Gas System Modelling with Hydrogen Injections and Gas Composition Tracking”, Applied Energy, 2021
S. Mhanna, et al., “Iterative LP-based Methods for the Multiperiod Optimal Electricity and Gas Flow Problem”, IEEE Trans. on Power Systems, 2021
Courtesy of Future Fuels CRC

## Slide 37: Acknowledgements
CSIRO and AEMO for the ongoing support on the topic of “Planning” as part of the GPST consortium
C4NET for the “ESP-V” project
The Future Fuels CRC
The incredible work of my incredible team!

## Slide 38: Thank you! Any question?